from			to			name
device	conn.	pin	device	conn.	pin
alarm device			pump pit	P9		S-ALARM
alarm device			pump pit	P10		S-ALARM
E-1	F4		ESz-1	J9	1-2	230V 4A AC L
E-1	line N		ESz-1	J8	1-4	N
E-1	line PE		ESz-1	J10	17	PE
E-1	Tr		ESz-1	J6	1	24V AC L1
E-1	Tr		ESz-1	J6	2	24V AC L2
ESz-1	J4	1	FE	F3-4		aux. contact NC (30V DC)
ESz-1	J4	2	FE	F3-4		aux. contact NC
ESz-1	J4	3	FE	F3		aux. contact NO
ESz-1	J4	4	FE	F3		aux. contact NO
ESz-1	J4	5	FE	F4		aux. contact NO
ESz-1	J4	6	FE	F4		aux. contact NO
ESz-1	J6	3	E-1	F4		aux. contact NC (30V DC)
ESz-1	J6	4	E-1	F4		aux. contact NC
ESz-1	J6	5	E-1	F4		aux. contact NO
ESz-1	J6	6	E-1	F4		aux. contact NO (30V DC)
ESz-1	J12	2	MM9A	P14		E-COM
ESz-1	J12	3	MM9A	P12		E-PMN
ESz-1	J12	4	MM9A	P13		E-PMX
ESz-1	J12	6	MM9A	P4		24V DC
ESz-1	J12	7	MM9A	P5		CI1
ESz-1	J12	8	MM9A	P6		CI2
ESz-1	J12	9	MM9A	P7		CI3
FE	F4		MM9A	P2		230V 6A AC
FE	line N		MM9A	P3		N
FE	line PE		MM9A	P1		PE
MM9A	P8		pump pit	P7		S-PMN
MM9A	P9		pump pit	P8		S-PMN
MM9A	P10		pump pit	P5		S-PMX
MM9A	P11		pump pit	P6		S-PMX
MM9A	P15		pump pit	P1		GND
MM9A	P16		pump pit	P2		VO1
MM9A	P17		pump pit	P3		VO2
MM9A	P18		pump pit	P4		VO3
MM9A	P19		pump pit	X1	1	WPO-N
MM9A	P20		pump pit	X1	2	WPO-L
MM9A	P21		pump pit	X1	3	WPO-PE